## Slide 1: RLE Compression using Verilog and Verification using Functional Simulation
3/8/2017

## Slide 2: Objectives
Learn to write Verilog for a custom design
Understand how to verify your design using functional simulation
Learn to write Verilog test bench for your design

## Slide 3: Run Length Encoding
Takes data stream and records how many bits
are the same
Output the value of the bit and the number of
iterations of that value
  ID Value
  Count Value

## Slide 4: Run Length Encoding (Contd..)
Input – 8 Bit data stream segments
Output – 24 Bit data
How does it work?
  First bit – ID Bit (0 or 1)
  Count value - 23 bits (Number of 0s or 1s)
More of same value in sequence, more data is saved
Worst Case - Interchanging data (01010101.....)

## Slide 5: Illustration
1
1
1
0
0
0
0
0
1
3
0
7
23bit
1bit
Original Data Stream Segment
Encoded Data Stream Segment
8bit
0
0
1
1
1
1
0
0
1
4
0
2
0
7

## Slide 6: RLE Implementation
Implemented using a state machine written in Verilog (provided)
  Understand the state diagram (appendix)
  State transitions provided
  Fill in the commented sections

## Slide 7: Functional Simulation
Technique to verify the functionality of a hardware design (Design verification)
Standard procedure followed in the industry before implementing in a target device
Provide the inputs to your design and check the outputs to confirm functionality
ModelSim from Mentor Graphics is a well known tool used in the industry

## Slide 8: ModelSim – Functional simulation tool
Two ways to perform the design verification
  Set the inputs through wave editor and observe the outputs
  Design a test bench for your design

## Slide 9: Wave Editor in ModelSim

## Slide 10: Test Bench
Verilog wrapper module which does the following
  Invokes the Design Under Test (DUT) - RLE
  Provides the inputs to the DUT
  Formats the outputs suitable for viewing
Verilog provides constructs such as procedural blocks and timing controls
Good source: https://people.ece.cornell.edu/land/courses/ece5760/Verilog/LatticeTestbenchPrimer.pdf

## Slide 11: Test Bench Template
Module ‘RLE_test’
Instance ‘RLE_top’
RLE Verilog netlist
module (DUT)
Procedural blocks
with test bench code
DUT inputs
DUT outputs

## Slide 12: Summary
To implement hardware for RLE
  Encoding is done in Hardware (Verilog)
Functional simulation
  Verify the design by providing the input stimulus and observe the output using Verilog test bench

## Slide 13
Appendix
Signals and their Description

## Slide 14: RLE Internal Signals
reg rd_reg
  connected to rd_req;
reg wr_reg
  Connected to wr_req;
reg [22:0] bit_count
  Stores number of same consecutive bit in bit stream
  value_type represent bit ID
reg value_type
  Bit ID

## Slide 15: RLE Internal Signals
reg [7:0] shift_buf
  Store 8 bit segment of bit stream comes from input side FIFO
  Will be shifted out to calculate number of bits
reg [3:0] shift_count
  Current shift amount of shift_buf
reg new_bitstream
  Indicate new bit sequence is starting
  Current encoded data segment is passed to output side FIFO

## Slide 16: RLE Internal Signals
reg [3:0] state
  Represent State.
  There are 9 states in total
reg [3:0] next_state
  Represent Next state

## Slide 17: RLE Interface - Input
input clk,rst
  clk and reset
input recv_ready
  Connected with (!fifo_empty) of input side FIFO
input send_ready
  Connected with (!fifo_full) of output side FIFO
input [7:0] in_data
  Input data from input side FIFO
  8 bit segment of original bit stream
input end_of_stream
  Indicate the end of bit stream
  Request flushing out the last segment

## Slide 18: RLE Interface - Output
output [23:0] out_data
  Output data to output side FIFO
  [23] has bit ID, [22:0] has bit counting value
output rd_req
  Read request for input side FIFO
output wr_req
  Write request for output side FIFO

## Slide 19
READ_INPUT
shift_buf = in_data
WAIT_INPUT
rd_reg = 0
REQUEST_INPUT
rd_reg = 1
shift_count = 0
COUNT_BITS
Increase bit_count
Set/reset
new_bitstream
SHIFT_BITS
Shift sift_buf
Increase
shift_count
Lookup
new_bitstream
COUNT_DONE
wr_reg = 1
WAIT_OUTPUT
wr_reg = 0
RESET_COUNT
bit_count = 0
INIT
bit_count = 0
shift_buf = 0
rd_reg = 0
wr_req_reg = 0
new_bitstream = 1
!recv_read
!recv_read&
end_of_stream&
bit_count != 0
new_bitstream
shift_count == 7
send_ready
end_of_stream

## Slide 20: RLE State in detail
INIT
  Initialize registers
REQUEST_INPUT
  Assert rd_req signal to FIFO by setting rd_reg
  FIFO takes rd_req signal at next clock
WAIT_INPUT
  1 cycle stall is needed
  De-assert rd_req by setting rd_reg
READ_INPUT
  FIFO provides valid data after taking rd_req
  shift_buf stores 8 bit input data

## Slide 21: RLE State in detail
COUNT_BITS
  Count number of consecutive bits in shift_buf
  If new type of bit starts, store bit ID in value_type register
  If current value_type and shift_buf[0] is not matched, notify current encoding is completed and new encoding will be started
SHIFT_BITS
  Right shift the shift_buf
  Increase shift_count
  Look up new_bitstream
COUNT_DONE
  Assert wr_req by setting wr_reg
  FIFO will take wr_req signal in next clock cycle

## Slide 22: RLE State in detail
WAIT_OUTPUT
  1 cycle stall is needed
  De-assert wr_req by setting wr_reg
RESET_COUNT
  Reset bit counting register after passing encoded data to output side FIFO

## Slide 23: Race Condition
Produces different simulation result from real hardware
Keeping verilog design guideline is important
always @(posedge clk)
a = b;
always @(posedge clk)
b = c;
Which statement will be executed first?
An Example

## Slide 24: Important Design Guideline for LAB 3
Do not mix BA and NBA in the same always block
Use BA for combinational circuit in given design
  State transition
Use NBA for sequential circuit in given design
  Updating registers