## Slide 1: ECE 354
Lab 4
HW/SW Compression and Decompression of Captured Image

## Slide 2: Objectives
Understand how to leverage the FPGA-based hardware acceleration in an SoC design.
Understand how communication is done between the FPGA fabric and the ARM hard core processor system (HPS) in an SoC board
Understand how to add new components to an existing QSYS design to implement new functionalities

## Slide 3: Overview
In this lab, you will do the following:
Implement new features by adding Verilog files into an existing Quartus project
  FIFO Buffer Modules
  RLE Compression Module (implemented in lab 3)
Use the RLE implemented on FPGA fabric to compress the captured image
Implement the RLE decompression algorithm using C on ARM HPS to recreate the original image and display on the monitor

## Slide 4: System Diagram
Picture data
Compressed picture data
Camera
Monitor
FPGA RLE Encoder
(Hardware)
RLE Decoder
(Software)
ARM
VGA Port
High Bandwidth Interconnect
SDRAM

## Slide 5: RLE Hardware Block Structure and Integration
ARM core
FIFO_send
FIFO_recv
RLE Unit
ODATA_PIO[7:0]
FIFO_IN_WRITE_REQ_PIO
FIFO_IN_FULL_PIO
IDATA_PIO[23:0]
RESULT_READY_PIO
FIFO_OUT_READ_REQ_PIO
RLE_RESET_PIO
FIFO_IN_ODATA[7:0]
FIFO_IN_READ_REQ
FIFO_IN_EMPTY
RLE_OUT[23:0]
RLE_DONE
FIFO_OUT_FULL
RLE_FLUSH_PIO

## Slide 6: FIFO Buffer
Saves data based on clock tick when write request signal is asserted
Holds buffered values in registers until requested from RLE
Outputs data in a specified way
  Same order in which it came into the buffer
  First in the buffer, first to come out (FIFO)
  Sends data only when requested by a signal
Used due to asynchronous signals and data sent from the software

## Slide 7: HPS-FPGA Lightweight Bridge
The ARM HPS does not have direct access to hardware instantiated on the FPGA fabric
Communication is done through the high bandwidth memory-mapped bus bridges
Tie the Avalon memory mapped slave connections of the PIOs to the Lightweight Bridge AXI Master connection in QSYS (detailed procedure provided in the lab instructions manual)

## Slide 8: Getting started - Hardware design
Copy the contents of lab 2 into a new folder and rename it as lab 4
Add the rle_enc.v that you designed in lab 3 and rle_fifo_8_24.v given to you into your Quartus project
Add the additional PIOs to the existing QSYS system
Modify DE1_SOC_With_D5M.v
    Instantiate your RLE unit and two FIFO modules
    Add the necessary wires for ARM-module and module-module connections
    Connect your Verilog hardware and QSYS system

## Slide 9: Signals in Block Structure (To be added in QSYS)
RESULT_READY_PIO
  Indicates that there is an encoded data segment in the FIFO. Note that this signal is active low since it is tied to the FIFO empty output.
RLE_FLUSH_PIO
  Used at the end of the bit-stream. RLE produces the final encoded data segment immediately with the last counting bit value.
RLE_RESET
  Signal for initializing RLE encoder. Assert and de-assert at the beginning of the program.
IDATA_PIO[23:0]
  Input ports to receive the encoded data.
  1 bit for bit ID, 23 bits for representing number of bits.
ODATA_PIO[7:0]
  Output ports to send original bit-stream. Data is sent in 8-bit segments.
FIFO_IN_FULL_PIO
  Indicates FIFO is full. Sending picture data stream should wait until this signal is de-asserted.
FIFO_IN_WRITE_REQ_PIO
  Asserted to write bitstream segment to FIFO in buffer. FIFO stores input data when this signal is asserted.
FIFO_OUT_READ_REQ_PIO
  Asserted when ARM wishes to read from the FIFO out. FIFO produces next data from the buffer when this signal is asserted.

## Slide 10: Hardware Design contd.,
Full source code for 8 bit and 24 bit FIFO will be provided
  rle_fifo_8_24.v
Use the RLE Verilog code that you implemented in Lab 3
Top-level module
  DE1_SOC_With_D5M.v
  You will need make modifications to connect your new hardware
Compile the design (Might take a while!)

## Slide 11: Software design - preprocessing of the captured image
Current image format uses 16 bits per pixel
Black and white image only needs one bit to convey all information for the pixel
Convert to a storage format that uses only 1 bit per pixel
Ex:
Pixel 1: 0000 0000 0000 0001
Pixel 2: 0000 0000 0000 0000
Pixel 3: 0000 0000 0000 0001
…
Becomes
101…….

## Slide 12: Software Design
Use Altera functions to send/receive data
  alt_write_byte()
  alt_read_byte()
  alt_read_word()
Send data to be compressed
  while(buffer_not_full){ alt_write_byte(data_pio_base, data); .....; }
Receive data from compression
  if(buffer_not_empty){ data = alt_read_word(dataout_pio_base); ....; }

## Slide 13: Software Design
Software must be able to decompress data
  Relatively easy
    Data tells you what to write
    Example: (10000000 00000000 00000111)
      First Value = 1
      Second Value = 7
      Write 1, 7 times
      Output: 1111111

## Slide 14: Deliverables
Implement a function in C to convert the captured color image to black and white on the ARM HPS and display the image on the monitor
Compress this image using the RLE in FPGA fabric
Implement a function in C to decompress the compressed image on the ARM HPS and display it on the monitor along with the compression ratio

## Slide 15: Tips
Go through the detailed instructions posted on the class website before starting the Lab 4
Compressed Data is variable length for every picture
  Data could be compressed smaller, or expanded into larger data
  Assume compressed data can be larger than the original picture data and do not fix the compressed output array size

## Slide 16: Summary
To implement hardware and software for RLE
  Encoding is done by Hardware
    GPIO is used
    Read/Write data from/to hardware is done by using ALTERA API
  Decoding is done by Software
The RLE implementation is added to Lab 2
  Take pictures and perform transformations
  Display the images before and after compression and decompression occur

## Slide 17: Extra credit
Re-do lab 4 but with Linux installed on the DE1-SoC board
Unlike bare-metal ARM HPS, Linux doesn’t have access to the physical memory space
Use a Linux kernel function mmap which maps the physical memory space to the virtual memory space
More resources will be posted in the future!

## Slide 18
Questions
Notes: 18

## Slide 19
Appendix
Notes: 19

## Slide 20: How to Add/Wire New Modules
Top Module wires the components together with the QSYS system
  DE1_SOC_With_D5M.v is the top module for the project
  Must add three components into the top module file
    2 Buffers
    1 RLE
To add a module, must follow certain format
  Module_File_Name Module_Name ( .input1 (wire1) .input2 (wire 2) .output1 (wire3) );
Computer_System is the QSYS system generated by QSYS
  Look at QSYS – Generate – Show Instantiation Template to view names of connections to be added

## Slide 21: Signals in Block Structure (Non-QSYS)
FIFO_IN_READ_REQ
  Asserted by the encoder when it is ready for the next bitstream segment.
FIFO_IN_EMPTY
  Indicates that the FIFO in buffer is empty. The RLE must wait until the FIFO in buffer is nonempty to request new data.
FIFO_IN_ODATA[7:0]
  Provides the next bit-stream segment to RLE unit when FIFO_IN_READ_REQ is asserted.
RLE_OUT[23:0]
  Passes the encoded data from the encoder to the FIFO out buffer.
RLE_DONE
  Indicates that the encoder unit is ready to output the next encoded segment. It is also used as a write assert signal for the FIFO out buffer.
FIFO_OUT_FULL
  Indicates that the FIFO out buffer is full. The RLE unit should wait until this signal is de-asserted to write its next prepared segment.